## Slide 1: Nets created with the same base name but different net types (scalar vs. bus net) Auto conflict resolution (same as Rename)
Top Design
netA
Merge
Design Partition cle_p2
netA
netB<0:3>
Design Partition cle_p1
netA
netB
Top Design
netA
netB_cle_p1
netB<0:3>

## Slide 2: Nets created with the same name but different signal types Auto conflict resolution (same as Skip)
Top Design
netA
Design Partition cle_p1
netA
netB
sigType: power
Design Partition cle_p2
netA
netB
sigType: clock
Top Design
netA
netB
sigType: power
Merge

## Slide 3: An Existing Net Is Renamed in two partitions Connectivity Name Conflict Action: Skip
Merge
Top Design
netA
netB
Design Partition cle_p1
netA
netB -> netB_p1
Design Partition cle_p2
netA
netB -> netB_p2
Top Design
netA
netB_p1

## Slide 4: An Existing Net Is Renamed in two partitions Connectivity Name Conflict Action: Replace
Merge
Top Design
netA
netB
Design Partition cle_p1
netA
netB -> netB_p1
Design Partition cle_p2
netA
netB -> netB_p2
Top Design
netA
netB_p2

## Slide 5: An Existing Net Is Renamed in two partitions Connectivity Name Conflict Action: Rename (Same as action Error, b/c one net cannot be renamed into two)
Merge
Top Design
netA
netB
Design Partition cle_p1
netA
netB -> netB_p1
Design Partition cle_p2
netA
netB -> netB_p2
Top Design
netA
netB
(Do not merge netB’s changes)

## Slide 6: An Existing Net Is Renamed in two partitions Connectivity Name Conflict Action: Error
Top Design
netA
netB
Design Partition cle_p1
netA
netB -> netB_p1
Design Partition cle_p2
netA
netB -> netB_p2
Top Design
netA
netB
(Stop merge)
Top Design
netA
netB_p2
(The last partition wins)
Error Action: Stop
Error Action: Continue
Merge

## Slide 7: Pins created with the same name Connectivity Name Conflict Action: Rename
Merge
Top Design
term1:pin1
Design Partition cle_p2
term1:pin1
term1:pin2
Design Partition cle_p1
term1:pin1
term1:pin2
Top Design
term1:pin1
term1:pin2
term1:pin2_cle_p2